## Slide 1: Lecture 2: Filters
Tom Jhou

## Slide 2: A few things before we start:
Update project using PyCharm’s blue arrow:
Accept default, click OK

## Slide 3: Launch Anaconda, then Jupyter:

## Slide 4: If it gets stuck, launch from start menu …:

## Slide 5: You should see your home folder:

## Slide 6: Navigate to Homework1.ipynb:

## Slide 8: Now back to our regularly scheduled programming…

## Slide 9: Filters enhance signals, reduce noise:
Found everywhere:
Sound/video processing: microphones, cameras, medical equipment, etc.
Analysis software
Biological systems (visual and auditory cortex)

## Slide 10: How do you define “noise”?
Depends on your goal.
“Noise” in one experiment may be “signal” in another.

## Slide 11: Imaging examples:
“Edge detection” filter
Notes: This works like a charm. Before filtering, the background noise ranges over several millivolts, while spikes are only about 300 microvolts.
After filtering, background noise is about 100 microvolts, while spikes are still about 300 microvolts.
We removed a lot of stuff, and drastically reduced the background noise while spikes are almost the same height as before.

## Slide 12: Example: neural spike detection:
Notes: This works like a charm. Before filtering, the background noise ranges over several millivolts, while spikes are only about 300 microvolts.
After filtering, background noise is about 100 microvolts, while spikes are still about 300 microvolts.
We removed a lot of stuff, and drastically reduced the background noise while spikes are almost the same height as before.

## Slide 13: “Sampling” turns real-world signals into lists of numbers that Python/MATLAB can work with
“Stem” plot
Notes: This works like a charm. Before filtering, the background noise ranges over several millivolts, while spikes are only about 300 microvolts.
After filtering, background noise is about 100 microvolts, while spikes are still about 300 microvolts.
We removed a lot of stuff, and drastically reduced the background noise while spikes are almost the same height as before.

## Slide 14: “staircase” plot
Notes: This works like a charm. Before filtering, the background noise ranges over several millivolts, while spikes are only about 300 microvolts.
After filtering, background noise is about 100 microvolts, while spikes are still about 300 microvolts.
We removed a lot of stuff, and drastically reduced the background noise while spikes are almost the same height as before.

## Slide 15: If sample rate is high, they blend together into a continuous line. But signal is still ultimately a list of numbers.
Notes: There are fast wiggles and slow wiggles. The background noise tends to have lots of slow wiggles, the spikes tend to have lots of fast wiggles. We can use this to our advantage.
There are 20,000 points shown. The sampling rate is 31.25kHz, so this is about 2/3 of a second in the top part, and 1/8 second in the bottom part.

## Slide 16: Perform “spectral analysis” of spikes vs noise
Spikes
Background “noise”
Notes: “Noise” is in quotation marks because it actually is a brain signal. It comes from neurons that are too far away from recording wire to be resolved independently.

## Slide 17: Spectral analysis is what a prism does: it “unmixes” colors:
Low frequencies
High frequencies
Notes: The function is easy to call, but you have to pay careful attention to the details of the frequencies that come out.

## Slide 18: Noise is predominantly low-frequency. If we remove it, spikes will “stick out” more.
Spikes
Background “noise”
Notes: “Noise” is in quotation marks because it actually is a brain signal. It comes from neurons that are too far away from recording wire to be resolved independently.

## Slide 19: How to do frequency analysis? FFT = “Fast Fourier Transform”
import numpy as np
y = np.fft.fft(waveform);
waveform = list of voltage samples at regular time intervals
y = list of amplitudes at regular frequency intervals
Notes: The function is easy to call, but you have to pay careful attention to the details of the frequencies that come out.

## Slide 20: FFT of sine wave …
Ignore the right half of FFT for now.
FFT of above
5 Hz sine wave,
Sampled at 100 Hz
Peak at 5 Hz
Notes: The function is easy to call, but you have to pay careful attention to the details of the frequencies that come out.

## Slide 21: FFT of square wave:
waveform
FFT
5 Hz square wave,
Sampled at 100 Hz
Peaks at 5, 15, 25, 35, 45 Hz
Notes: The function is easy to call, but you have to pay careful attention to the details of the frequencies that come out.

## Slide 22: Basically, a square wave is really a combination of sinusoidal harmonics:
Sine waves, odd harmonics only
Cumulative sum:
5 Hz
15 Hz
25 Hz
35 Hz
45 Hz
etc…
Notes: Note that the sine wave amplitudes are exactly inversely proportional to the frequency, i.e. they get smaller as frequency goes up. The “discrepancy” between sinusoidal sum and “true” square wave gets smaller and smaller as well.

## Slide 23: By adjusting amplitudes, can make triangle instead of square wave
Square wave: Harmonic amplitudes = 1/n, n = 1, 3, 5, …
Triangle wave: nth harmonic amplitude = (-1)n/n2, n = 1, 3, 5, …
Negative amplitude for harmonics 3, 7, 11, etc
Notes: Note that the sine wave amplitudes are exactly inversely proportional to the frequency, i.e. they get smaller as frequency goes up. The “discrepancy” between sinusoidal sum and “true” square wave gets smaller and smaller as well.

## Slide 24: Adding even harmonics gives sawtooth wave:
Notes: Note that the sine wave amplitudes are exactly inversely proportional to the frequency, i.e. they get smaller as frequency goes up. The “discrepancy” between sinusoidal sum and “true” square wave gets smaller and smaller as well.

## Slide 25: By modifying phase and amplitude, can build any waveform
https://www.youtube.com/watch?v=ds0cmAV-Yek
Notes: Destin doesn’t explain one very critical item, which is that the rotational speeds of the various circles are all FIXED INTEGER MULTIPLES of each other. The first circle rotates at some constant speed. The second circle rotates at twice that speed, the third circle rotates at 3 times the speed, and so on. The shape is entirely defined by the diameters (amplitudes) of the circles.

## Slide 26: FFT of neural recording
Spikes
EEG
Notes: There are fast wiggles and slow wiggles. The background noise tends to have lots of slow wiggles, the spikes tend to have lots of fast wiggles. We can use this to our advantage.
There are 20,000 points shown. The sampling rate is 31.25kHz, so this is about 2/3 of a second in the top part, and 1/8 second in the bottom part.

## Slide 27: Noise has a lot of low frequencies (slow wiggles). Can remove them with “high-pass” filter.
Spikes
Background
Removing low frequencies will get rid of a LOT of background, but much less signal

## Slide 28: Filters are never perfect. There is “transition” from “pass” to “stop” bands
Output in the stop band is lower, but not zero.
Frequencies just above the cutoff frequency are not attenuated as effectively as those much further above.
100% pass
70.7% pass

## Slide 29: Note the “decibel” notation:
dB = 20 * log_10.
Why 20, and not 10?
Because power = amplitude2, so 10x amplitude increase gives 100x power increase.

## Slide 30: 3dB is the “half power” point:
This is where amplitude is 70.7% of max.
20 * log(0.707) = -3.01
Power = amplitude2, and (0.707)2 = 0.5

## Slide 31: Other standard filter types
Any shape is possible, including multiple pass bands, or arbitrary shapes.
“Roll-off” rate varies with filter type - can be shallow or steep.

## Slide 32: Why did I plot log axes? To avoid smushing low frequencies together:
Spikes
EEG
Linear axes
Spikes
EEG
Log axes
Notes: “Noise” is in quotation marks because it actually is a brain signal. It comes from neurons that are too far away from recording wire to be resolved independently.

## Slide 33: Absolute vs relative change
10-fold
range
10-fold
range
10-fold
range
400Hz
range
400Hz
range
400Hz
range
400Hz
range
Linear axes show absolute change
Log axes show relative change
Notes: “Noise” is in quotation marks because it actually is a brain signal. It comes from neurons that are too far away from recording wire to be resolved independently.

## Slide 34: Human perception often logarithmic: Weber’s law
Notes: “Noise” is in quotation marks because it actually is a brain signal. It comes from neurons that are too far away from recording wire to be resolved independently.

## Slide 35: Python code:
kernel = signal.firwin(n, cutoff_frequency*2/sampleRate, pass_zero = False)
output = np.convolve(wave, kernel);
Notes: This works like a charm. Before filtering, the background noise ranges over several millivolts, while spikes are only about 300 microvolts.
After filtering, background noise is about 100 microvolts, while spikes are still about 300 microvolts.
We removed a lot of stuff, and drastically reduced the background noise while spikes are almost the same height as before.

## Slide 36: Voltage histograms
Background
Spikes
Voltage (mV)
Before filtering
Notes: These are histograms of the voltage ranges. Before filtering, background and spikes range over several millivolts, and overlap.
After filtering, spike peaks are separable from background voltages. We can draw a somewhat arbitrary vertical threshold (blue dotted line) that “detects” most of the spikes while “rejecting” most of the background.

## Slide 37: Voltage histograms
Spike peaks
Background
Voltage (mV)
After filtering
False positives
True positives
Detection threshold
Notes: These are histograms of the voltage ranges. Before filtering, background and spikes range over several millivolts, and overlap.
After filtering, spike peaks are separable from background voltages. We can draw a somewhat arbitrary vertical threshold (blue dotted line) that “detects” most of the spikes while “rejecting” most of the background.

## Slide 38: Let’s look at a noisier example:
Spikes
Background
Voltage (mV)
Detection threshold
More selective
(Fewer false positives,
but also more false negatives)
More permissive
Fewer false negatives,
but also more false pos.)
False negatives
True negatives
Notes: These are histograms of the voltage ranges. Before filtering, background and spikes range over several millivolts, and overlap.
After filtering, spike peaks are separable from background voltages. We can draw a somewhat arbitrary vertical threshold (blue dotted line) that “detects” most of the spikes while “rejecting” most of the background.

## Slide 39: “Receiver operator characteristic” (ROC) expresses tradeoff
Background
Voltage (mV)
Detection threshold
More selective
(Fewer false positives,
but also more false negatives)
More permissive
Fewer false negatives,
but also more false pos.)
More selective
More permissive
False positives
True positives
Spikes
Notes: These are histograms of the voltage ranges. Before filtering, background and spikes range over several millivolts, and overlap.
After filtering, spike peaks are separable from background voltages. We can draw a somewhat arbitrary vertical threshold (blue dotted line) that “detects” most of the spikes while “rejecting” most of the background.

## Slide 40: “Receiver operator characteristic” (ROC) expresses tradeoff
Spikes
Voltage (mV)
True positives
Detection threshold
More selective
(Fewer false positives,
but also more false negatives)
More permissive
Fewer false negatives,
but also more false pos.)
More selective
More permissive
False positives
Background
Notes: These are histograms of the voltage ranges. Before filtering, background and spikes range over several millivolts, and overlap.
After filtering, spike peaks are separable from background voltages. We can draw a somewhat arbitrary vertical threshold (blue dotted line) that “detects” most of the spikes while “rejecting” most of the background.

## Slide 41: Filtering greatly improved detection, but still short of perfection
More selective
More permissive
y=x, random classification
Detecting ~25% of spikes, and ~5% of noise.
Highest signal/noise ratio (5:1).
Perfect classification:
Detect 100% of signal, 0% of background.
Can’t get here with this dataset.
p = 0.05 (publication standard)
Before filtering
After filtering
Notes: These are histograms of the voltage ranges. Before filtering, background and spikes range over several millivolts, and overlap.
After filtering, spike peaks are separable from background voltages. We can draw a somewhat arbitrary vertical threshold (blue dotted line) that “detects” most of the spikes while “rejecting” most of the background.

## Slide 42: Filtering is big help, but not magic. Often you need a better experiment (better method, or move probe closer to neurons)

## Slide 43: Area under curve (AUC) is proportional to Mann-Whitney “U”
Notes: These are histograms of the voltage ranges. Before filtering, background and spikes range over several millivolts, and overlap.
After filtering, spike peaks are separable from background voltages. We can draw a somewhat arbitrary vertical threshold (blue dotted line) that “detects” most of the spikes while “rejecting” most of the background.

## Slide 44: Python code:
kernel = scipy.signal.firwin(n, cutoff_frequency*2/sampleRate, pass_zero=False)
output = np.conv(input_signal, kernel);

## Slide 45: “firwin” function:
kernel = scipy.signal.firwin(n, cutoff_frequency*2/sampleRate, pass_zero=False)
n is filter “order”
cutoff_frequency is half-power frequency (transition from pass to stop bands)

## Slide 46: pass_zero argument specifies low vs high-pass behavior
kernel = scipy.signal.firwin(n, cutoff_frequency*2/sampleRate, pass_zero=False)
pass_zero=True
pass_zero=False
0 Hz
0 Hz

## Slide 47: “convolve” function does the filtering:
kernel = fir1(n, cutoff_frequency*2/sampleRate, pass_zero=False)
output = np.convolve(input_signal, kernel)
kernel is also called “impulse function”
“convolving” input with kernel produces filtered output.

## Slide 48: Higher filter order n gives sharper transition from pass to reject
N=5
N=100
N=20
N=2
N=10
Pass band
Reject band

## Slide 49: Low-pass filter
N=5
N=100
N=2

## Slide 50: But: high order filters produce delays and other distortions
Before
filter
After
filter
Output is time-delayed (easy to compensate).
Biphasic waveform might become triphasic (NOT easy to correct)
High-order filters distort more than low order
High-pass filters distort more than low-pass.
Notes: The original spike (brown) is shifted in time and is now triphasic instead of biphasic. Actually, it is almost quadruphasic, as there is a slight backlash to the initial AHP.
The time shift is easy to fix – just subtract. The distortion is much harder to fix. Theoretically you can run it back through a lowpass filter, but that brings back some of the noise you got rid of.
Distortion may or may not be a problem. This depends on the question you are asking. If you just want to know firing rate and spike latency, you don’t have to worry.

## Slide 51: Another distortion:
“Sample rate” is finite. Some information always lost
time
time

## Slide 52: “Aliasing” occurs at low sample rates
Sine wave = 10kHz.
Sample rate = 40kHz
GOOD!
Sine wave = 30kHz.
Sample rate = 40kHz
BAD!
Notes: Note that the 30kHz wave looks exactly like the 10kHz wave when sampled at 40kHz. This is the “aliasing”, where one wave looks like another.

## Slide 53: Aliasing
At 40kHz sample rate,
10kHz, 30kHz look same

## Slide 54: Aliasing
19kHz, 21kHz look same
5kHz, 35kHz look same
1kHz, 39kHz look same
Max unambiguously detected frequency is 20 kHz.
“Nyquist” frequency

## Slide 55: Typically need analog filter before digital sampling
https://community.sw.siemens.com/s/article/data-acquisition-anti-aliasing-filters
Low-pass ANALOG filter

## Slide 56: If frequencies < Nyquist, original wave can be interpolated perfectly from samples (via sinc function)
https://demonstrations.wolfram.com/SincInterpolationForSignalReconstruction/
Blue = original signal. Red dots = sampled.
Magenta = interpolated from samples using sinc function.

## Slide 57: Homework, due in 1 week
Update the github repository. You should see a folder called Class2, and a Python file called Homework2.py
Task 1: write code to remove the noise and identify the underlying musical piece.
Task 2: Plot Fourier transforms of wave before and after filtering.

## Slide 58: The end. Ignore any slides after this one.

## Slide 59: A few notes about Python functions:
Function name
Package name

## Slide 60: Arguments are distinguished by their position (1st, 2nd, 3rd) or name:
First argument (no name)
2nd argument (named)
3rd argument (named)

## Slide 61: Named arguments can be in any order:
np.mean(calcium, axis = 0, dtype = np.float32)
np.mean(calcium, dtype = np.float32, axis = 0)

## Slide 62: Skipped arguments take default value:
Default values if skipped

## Slide 63: Another common way to call functions:
np.mean(calcium, axis = 0)
# The following is functionally equivalent:
calcium.mean(axis=0)
This works because of something called “object oriented programming”.

## Slide 64: Think of “objects” as “smart” variables:

## Slide 65: The code:
% Generate/plot 5 Hz square wave
t = np.arange(100)/100
y = scipy.signal.square(t*5*2*pi);
np.step(t, y)
% Calculate/plot FFT
f = np.fft.fft(y);
np.plot(abs(f))
waveform
FFT
Notes: The function is easy to call, but you have to pay careful attention to the details of the frequencies that come out.

## Slide 66: Convolution, FFT, are all “linear” functions

## Slide 67: Much of nature is non-linear
But non-linear math is freakishly complex, so we try to make linear approximations wherever possible.
Many things are linear, up to a point.

## Slide 68: Algebraic definition of linearity:
  All terms square and higher are zero:

## Slide 69: Most general definition of linearity
A function f is linear if and only if:
  f(x + y) = f(x) + f(y) f (of sums) = sum (of f’s)
  af(x) = f(ax) Scalability
Notes: If you want to convolve A with the sum of B and C, you can break it into two easier tasks. First convolve A with B, then A with C, then add the two results.
All linear functions are handy this way, they can always be broken down into parts, solved independently, then added back together.

## Slide 70: Good overview of filtering:
https://www.sciencedirect.com/science/article/pii/S0896627319301746

## Slide 71: Why “abs”?
% Calculate/plot FFT
f = fft(y);
plot(abs(f))
FFT
Notes: The function is easy to call, but you have to pay careful attention to the details of the frequencies that come out.