## Slide 1: Dot products and correlations
Tom Jhou

## Slide 2: Homework review:

## Slide 3: Did you notice that output is longer than input?
Original audio clip
Recovered audio clip

## Slide 4: Let’s revisit convolution with finite kernel length = 5

## Slide 5: t = 0

## Slide 6: t = 1

## Slide 7: t = 2

## Slide 8: t = 3

## Slide 9: t = 4

## Slide 10: t = 5

## Slide 11: t = 6

## Slide 12: t = 7

## Slide 13: t = 8

## Slide 14: t = 9

## Slide 15: t = 10

## Slide 16: t = 11

## Slide 17: t = 12

## Slide 18: Output goes from t=0 to 12, i.e. has 13 samples.
Input = 9 samples
Kernel = 5 samples
Output length
= 9 + 5 – 1
= 14 – 1
= 13

## Slide 19: Did anybody plot the kernel?:
plt.plot(kernel)

## Slide 20: Note peak at exact center
plt.plot(kernel)
50,001
100,001

## Slide 21: Zoom into center:
plt.plot(kernel[49900:50100])

## Slide 22: Two component: central peak, plus side wiggles.
plt.plot(kernel[49900:50100])

## Slide 23: Consider central peak alone:

## Slide 24: Make smaller example: g2 = 1, everything else = 0

## Slide 25: t = 0, output = 0

## Slide 26: t = 1, output = 0

## Slide 27: t = 2, output = f0

## Slide 28: t = 3, output = f1

## Slide 29: t = 4, output = f2

## Slide 30: t = 5, output = f3

## Slide 31: t = 6, output = f4

## Slide 32: t = 7, output = f5

## Slide 33: t = 8, output = f6

## Slide 34: t = 9, output = f7

## Slide 35: t = 10, output = f8

## Slide 36: Output is delayed by 2 samples, but otherwise unchanged.
Delay = (kernel length – 1) / 2
In small example, delay = (5-1)/2 = 2
In homework, delay = (100000-1)/2 = 50,000

## Slide 37: Now consider side wiggles:

## Slide 38: The wiggle frequency matches noise frequency:
Kernel (minus central peak)
2kHz noise

## Slide 39: This is a band-pass filter.
Kernel (minus central peak)
Convolving this with 2kHz sinusoid gives “constructive interference”.
Other frequencies will give destructive interference, and be attenuated.

## Slide 40: Note that it has negative value where the central spike was positive
Kernel (minus central peak)
This causes 2kHz components to be subtracted, rather than added

## Slide 41: This kernel takes original signal, and subtracts 2kHz components
Result is a “band-stop” filter.

## Slide 42: Fourier transform can be inverted
f1 = np.fft.fft(x)
f2 = np.fft.ifft(y)
f2 will look just like x

## Slide 43: One way to implement filter is to take fft, “edit” the frequencies, then invert

## Slide 44: Convolution and cross-correlation are very related:
Convolution:
Cross-correlation:
The only difference is that in convolution, g is flipped backwards.

## Slide 45: t = 0

## Slide 46: t = 1

## Slide 47: t = 2

## Slide 48: t = 3

## Slide 49: t = 4

## Slide 50: These are all pairwise sum of products: also called “dot” products
If a and b are vectors:
  a = [a0, a1, a2, … an-1]
  b = [b0, b1, b2, … bn-1]
then dot product of a and b is:

## Slide 51: f∙g = cross-correlation at t = 0

## Slide 52: Geometrical interpretation of dot product
Vector with n elements can be represented by arrow in n-dimensional space.
Arrow has direction and length
Notes: All these vectors have the same magnitude = 5.

## Slide 53: Dot product of vector with self = length2
Let A = [x, y] be a two-dimensional vector
Then A • A = x2 + y2 = hypotenuse2

## Slide 54: Two vectors of magnitude 5:
a = (5, 0)
a • a = 25 = |a|2
b = (4, 3)
b • b = 42 + 32
= 16 + 9
= 25
= |b|2
Notes: All these vectors have the same magnitude = 5.

## Slide 55: Orthogonal vectors
(+3,+4) • (-4,-3) = -12 + 12
= 0
Notes: All these vectors have the same magnitude = 5.

## Slide 56: Opposite direction vectors
(3,4) • (-3,-4) = -9 – 16
= - 25
Notes: All these vectors have the same magnitude = 5.

## Slide 57: Neither parallel nor orthogonal
a = (+5, 0)
b = (+4, +3)
a • b = 5 * 4 = 20
Notes: All these vectors have the same magnitude = 5.

## Slide 58: Rewrite using trigonometry
=36.87°
a = (+5, 0)
b = (+4, +3)
cos θ = adjacent / hypotenuse = 4/|b|
4 = |b|cos θ
a • b = sum of pairwise products
= 5 * 4
= |a|*(|b|cos θ)
= |a||b|cos θ
|b|=5
bx =4
Notes: All these vectors have the same magnitude = 5.

## Slide 59: Cosine function is +1 when θ = 0, zero when θ = 90 or 270.
90 deg = orthogonal
180 deg = opposite directions
0 deg = parallel
36.9 deg (example we just saw)
Notes: All these vectors have the same magnitude = 5.

## Slide 60: Can prove (not here) that cosine formula is true for any 2 vectors, in any number of dimensions:
  a • b = |a||b|cos θ
where θ is angle between a, b in n-dimensional space.

## Slide 61: How do we define θ if dimensions>3?
There will be some 2D plane containing both vectors, even if embedded in a high-dimensional space.
Define angle in this plane

## Slide 62: Terminology: “unit” vector, length = 1.0
Can create by dividing any vector by its own magnitude.
b̂ = b / |b| = (4/5, 3/5) = (0.8, 0.6)
Verify:
0.82 + 0.62 = 0.64 + 0.36 = 1.00
b̂
(0.8, 0.6)
Notes: All these vectors have the same magnitude = 5.

## Slide 63: Dot product with any unit vector = length of shadow
Dot product of “a” with unit vector “u” is length of the “shadow” of “a” onto “u”
Notes: Using the definition of cosine, we can “prove” the dot product for the special case where one vector lies along the x-axis.

## Slide 64: How can we visualize dot product involving > 3 dimensions?
?
5D, etc
?

## Slide 65: Each axis must be perpendicular to the existing ones. Can’t do this after 3
?
5D, etc
?

## Slide 66: Try a completely different approach
Chart: Elements of A
| -2 | -1 | 1 | 2
 | -2 | -1 | 1 | 2
A | B
-2 | -2
-1 | -1
1 | 1
2 | 2
a4*b4 = +4
a3*b3 = +1
a2*b2 = +1
a1*b1 = +4

## Slide 67: Two 4-D vectors define 4 pairs of x,y coordinates
Chart: Elements of A
| -2 | -1 | 1 | 2
 | -2 | -1 | 1 | 2
A | B
-2 | -2
-1 | -1
1 | 1
2 | 2

## Slide 68: Dot product = + 10
Chart: Elements of A
| -2 | -1 | 1 | 2
 | -2 | -1 | 1 | 2
A | B
-2 | -2
-1 | -1
1 | 1
2 | 2
All pairwise products are positive in top-right, and bottom-left quadrants
a4*b4 = +4
a3*b3 = +1
a2*b2 = +1
a1*b1 = +4

## Slide 69: Rearrange “b” to get new points:
Chart: Elements of A
| -2 | -1 | 1 | 2
 | 2 | 1 | -1 | -2
A | B
-2 | 2
-1 | 1
1 | -1
2 | -2
Dot product = - 10
Note that points in lower right, and upper left, contribute to negative sum
a4*b4 = -4
a3*b3 = -1
a2*b2 = -1
a1*b1 = -4

## Slide 70: Now dot product = -10
Chart: Elements of A
| -2 | -1 | 1 | 2
 | 2 | 1 | -1 | -2
A | B
-2 | 2
-1 | 1
1 | -1
2 | -2
a4*b4 = -4
a3*b3 = -1
a2*b2 = -1
a1*b1 = -4
All pairwise products are positive in top-right, and bottom-left quadrants

## Slide 71: 25-D example:
(a1, a2, a3, …) • (b1, b2, b3, …) =
Two 25-D vectors, A, B
A | B
0.256574 | -0.47409
-1.06162 | 0.104613
0.205486 | 1.000592
1.381874 | 1.641875
-0.3789 | -1.03427
1.32869 | 0.189985
1.344438 | 1.911619
1.461591 | 0.914581
1.554256 | 0.737026
0.889833 | 0.963659
-1.24735 | -0.24158
-0.75902 | -1.52722
-1.43461 | -0.8119
-0.00607 | 0.716201
-0.26062 | -0.11456
-0.54498 | -1.19385
0.328155 | 1.284383
-1.16679 | -0.55996
-0.05578 | -0.48953
-1.24326 | -0.80473
1.313789 | 1.361102
0.58111 | -0.63932
-0.06765 | -0.30031
-1.54698 | -0.91348
-0.87219 | -1.72084
Chart: 25-D vectors
| 0.25657429222571587 | -1.0616186078023999 | 0.20548610881223517 | 1.381873558925689 | -0.37889540538810246 | 1.3286902647263592 | 1.34443829699211 | 1.4615911958883132 | 1.5542555527654103 | 0.88983253333035262 | -1.247353014697145 | -0.75901640962667283 | -1.4346057042290985 | -6.0702136298166273E-3 | -0.2606151521556565 | -0.54498307370183352 | 0.32815492288073611 | -1.1667874356283112 | -5.5784708576388488E-2 | -1.2432553696370807 | 1.3137888985724597 | 0.58111047073829691 | -6.7645988932086079E-2 | -1.5469755707961184 | -0.8721894410569665
 | -0.47409 | 0.10461 | 1.0006 | 1.6419 | -1.0343 | 0.18998 | 1.9116 | 0.91458 | 0.73703 | 0.96366 | -0.24158 | -1.5272 | -0.8119 | 0.7162 | -0.11456 | -1.1938 | 1.2844 | -0.55996 | -0.48953 | -0.80473 | 1.3611 | -0.63932 | -0.30031 | -0.91348 | -1.7208

## Slide 72: Take a look at formula for Pearson’s cross-correlation “r”:
From Wikipedia:
Chart: 25-D vectors
| 0.25657429222571587 | -1.0616186078023999 | 0.20548610881223517 | 1.381873558925689 | -0.37889540538810246 | 1.3286902647263592 | 1.34443829699211 | 1.4615911958883132 | 1.5542555527654103 | 0.88983253333035262 | -1.247353014697145 | -0.75901640962667283 | -1.4346057042290985 | -6.0702136298166273E-3 | -0.2606151521556565 | -0.54498307370183352 | 0.32815492288073611 | -1.1667874356283112 | -5.5784708576388488E-2 | -1.2432553696370807 | 1.3137888985724597 | 0.58111047073829691 | -6.7645988932086079E-2 | -1.5469755707961184 | -0.8721894410569665
 | -0.47409 | 0.10461 | 1.0006 | 1.6419 | -1.0343 | 0.18998 | 1.9116 | 0.91458 | 0.73703 | 0.96366 | -0.24158 | -1.5272 | -0.8119 | 0.7162 | -0.11456 | -1.1938 | 1.2844 | -0.55996 | -0.48953 | -0.80473 | 1.3611 | -0.63932 | -0.30031 | -0.91348 | -1.7208

## Slide 73: Remember that indicates mean of all elements in .
Chart: 25-D vectors
| 0.25657429222571587 | -1.0616186078023999 | 0.20548610881223517 | 1.381873558925689 | -0.37889540538810246 | 1.3286902647263592 | 1.34443829699211 | 1.4615911958883132 | 1.5542555527654103 | 0.88983253333035262 | -1.247353014697145 | -0.75901640962667283 | -1.4346057042290985 | -6.0702136298166273E-3 | -0.2606151521556565 | -0.54498307370183352 | 0.32815492288073611 | -1.1667874356283112 | -5.5784708576388488E-2 | -1.2432553696370807 | 1.3137888985724597 | 0.58111047073829691 | -6.7645988932086079E-2 | -1.5469755707961184 | -0.8721894410569665
 | -0.47409 | 0.10461 | 1.0006 | 1.6419 | -1.0343 | 0.18998 | 1.9116 | 0.91458 | 0.73703 | 0.96366 | -0.24158 | -1.5272 | -0.8119 | 0.7162 | -0.11456 | -1.1938 | 1.2844 | -0.55996 | -0.48953 | -0.80473 | 1.3611 | -0.63932 | -0.30031 | -0.91348 | -1.7208

## Slide 74: Suppose both vector means = 0:

## Slide 75: Can simplify even more:

## Slide 76: Remember from slide #60:

## Slide 77: Pearson’s r = cos θ:
Pearson’s r is basically a normalized dot product.
Both measure pairwise similarity between sets of numbers.
Most similar
Most inversely similar
Not similar at all

## Slide 78: Dot products in Python

## Slide 79: Sometimes we need to do a lot of dot products:

## Slide 80: Conventional way to write dot product
= 1 * 9 + 2 * 6 + 3 * 3 = 9 + 12 + 9 = 30
First vector drawn horizontally, second one is vertical.
This order is very important.

## Slide 81: The end

## Slide 82: Matrix multiplication in Python