## Slide 1: Deep dive into Fourier transforms
Tom Jhou

## Slide 2: What is inside the FFT “magic box”?
Surprisingly simple formula:
N = number of samples.
xn = list of waveform voltages n = 0, 1, 2, … N-1
Xk = list of frequency values k = 0, 1, 2, … N-1

## Slide 3: First, a refresher on complex numbers
Complex number plane is two-dimensional
Vertical axis = “i”, where
Complex numbers have magnitude and PHASE
A = 2 + 5i
Real(A) = 2
Imag(A) = 5
Abs(A) = sqrt(2*2 + 5*5)
= sqrt(29)
= 5.39
2+5i
Notes: The function is easy to call, but you have to pay careful attention to the details of the frequencies that come out.

## Slide 4: Euler’s formula:

## Slide 5: Euler’s identity:
Combines the four most important constants in all of mathematics, each of which was a landmark discovery:
e, , i, and -1

## Slide 6: Compare sine to cosine wave.
Magnitude is same, but switches from real to imaginary
Imaginary / real components determine PHASE of sinusoid
FFT, real
FFT, imaginary
Notes: The function is easy to call, but you have to pay careful attention to the details of the frequencies that come out.

## Slide 7: Transform can be inverted …
Fourier transform:
Inverse Fourier transform:

## Slide 8: Work this out one term at a time …
The very first frequency component is simply the sum of input values.

## Slide 9: Can rewrite as matrix multiplication

## Slide 10: Next frequency term…

## Slide 11: Continuing along …
“Real” component:
“Imaginary” component:

## Slide 12: Real component with N = 100
Cosine
Sine
…

## Slide 13: This is yet another dot product

## Slide 14: Fourier transform
Frequency amplitude Xk is dot product of input with cosine/sine waves of frequency:
frequency = 0
f = sampleRate/n
2f
3f
4f
5f
6f
7f
8f
9f

## Slide 15: A collection of dot products = matrix multiplication

## Slide 16: Review of geometric interpretation of dot product as projection of one vector onto another vector
Unit vector “u” has length 1.
Vector “a” can be projected onto “u”
Projection is
Notes: Using the definition of cosine, we can “prove” the dot product for the special case where one vector lies along the x-axis.

## Slide 17: Dot product of any two rows in Fourier matrix = 0
A = [a0, a1, a2 … a99] = 1 Hz sine wave
B = [b0, b1, b2, … b99] = 10 Hz sine wave
Dot product = a0*b0 + a1*b1 + a2*b2 + a3*b3 + … + a99*b99
= sum of the black values below = 0

## Slide 18: Dot product of any Fourier matrix row with itself (actually its complex conjugate) = N
Dot product = a02 + a12 + a22 + a32 + … + a992
= sum of the black values below = 50

## Slide 19: Dot product of sine and cosine is zero because they are 90 degrees out of phase.
Sum of black values = 0

## Slide 20: Note:
xn = list of values at times: n = 0, 1, 2, … N-1
Xk = list of values at frequencies: k = 0, 1, 2, … N-1
We used normalized units 0, 1, 2, …. What are the “real” units, in seconds and Hertz?

## Slide 21: Time interval is reciprocal of sample rate
E.g. if sample rate = 100 Hertz, then interval between timestamps is 1/F = 0.01 sec

## Slide 22: Frequency interval is 1/T, where T is duration of input vector in seconds
# of samples N = F * T.
Highest frequency is (N-1)/T = , just slightly less than the sample rate F
Nyquist frequency = F/2
Frequency = F – 1/T
 N = 100 samples 

## Slide 23: For example …
List of times: seconds
List of frequencies:
Slightly < T
Slightly < F
Last value at 99Hz, not 100!
Last value at 0.99sec, not 1.00!
First value at t=0
Notes: In theory, you could add one more time sample, giving 101 samples with the last sample at 1.00 seconds.
But the FFT will still stop one sample short of 100 Hz. And now T = 1.1, so that list of frequencies is a very odd set of numbers.

## Slide 24: We’re not actually missing last time point. See staircase plot:
100th value starts at t=0.99sec,
Staircase “step” extends until t=1.00sec
First value starts at t=0
Staircase “step” extends until t=0.01
Notes: In theory, you could add one more time sample, giving 101 samples with the last sample at 1.00 seconds.
But the FFT will still stop one sample short of 100 Hz. And now T = 1.1, so that list of frequencies is a very odd set of numbers.

## Slide 25: Another way to look at Fourier transform
Twenty minute video …
https://www.youtube.com/watch?v=spUNpyF58BY&t=9s

## Slide 26: Convolution conceptualization #3:
Make polynomial having coefficients f, g:
F(z) = f0 + f1x + f2x2 + f3x3 + …
G(z) = g0 + g1x + g2x2 + g3x3 + …
(We omit negative time values for now)
This is the “z” transform. Converts a list of numbers into a function of “z” having those numbers as coefficients of z0, z1, z2, z3, z4, …

## Slide 27
By historical convention, we use “z” instead of “x”, but same idea:
F(z) = f0 + f1z + f2z2 + f3z3 + …
G(z) = g0 + g1z + g2z2 + g3z3 + …
This is the “z” transform. Converts a list of numbers into a function of “z”.

## Slide 28: Multiply F(z)G(z):
F(z) = f0 + f1z + f2z2 + f3z3 + …
G(z) = g0 + g1z + g2z2 + g3z3 + …
Use distributive property:
(X + Y + Z + W + …)*A = XA + YA + ZA + WA + …
F(z)G(z) = f0G(z)+ f1zG(z) + f2z2G(z) + f3z3G(z) + …
= f0(g0 + g1z + g2z2 + g3z3 + …)
+ f1z(g0 + g1z + g2z2 + g3z3 + …)
+ f2z2(g0 + g1z + g2z2 + g3z3 + …)
+ f3z3(g0 + g1z + g2z2 + g3z3 + …)
+ …
Notes: The distributive property looks a lot like the linearity property you saw a few slides ago. If you want to calculate the product of A times the sum of other numbers (X and Y), you can either add them first, then multiply by A, or you can play the divide and conquer game, and multiply the individual numbers by A, then take the sum. As with convolution, or any other linear function, you can add first, then multiply, or multiply first, then add.

## Slide 29: Distribute a second time:
F(z)G(z) = f0(g0 + g1z + g2z2 + g3z3 + …)
+ f1z(g0 + g1z + g2z2 + g3z3 + …)
+ f2z2(g0 + g1z + g2z2 + g3z3 + …)
+ f3z3(g0 + g1z + g2z2 + g3z3 + …)
+ …
F(z)G(z) = f0g0 + f0g1z + f0g2z2 + f0g3z3 + …
+ f1g0z + f1g1z2 + f1g2z3 + f1g3z4 + …
+ f2g0z2 + f2g1z3 + f2g2z4 + f2g3z5 + …
+ f3g0z3 + f3g1z4 + f3g2z5 + f3g3z6 + …
+ …
Sum of subscripts = exponent of z

## Slide 30: Group by powers of z:
F(z)G(z) = f0g0 + …
+ (f1g0 + f0g1 )z + …
+ (f2g0 + f1g1 + f0g2)z2 + …
+ (f3g0 + f2g1 + f1g2 + f0g3)z3 + …
+ (f4g0 + f3g1 + f2g2 + f1g3 + f0g4)z4 + …
…
Hmmm, that sounds like a convolution …
Coefficient of zn
is sum of pairwise products
whose subscripts sum to n

## Slide 31: It’s the same sum we saw with convolution
 | g[0] | g[1] | g[2] | g[3]
f[0] | f[0]*g[0] | f[0]*g[1] | f[0]*g[2] | f[0]*g[3]
f[1] | f[1]*g[0] | f[1]*g[1] | f[1]*g[2] | f[1]*g[3]
f[2] | f[2]*g[0] | f[2]*g[1] | f[2]*g[2] | f[2]*g[3]
f[3] | f[3]*g[0] | f[3]*g[1] | f[3]*g[2] | f[3]*g[3]
Sum of subscripts = 0
Sum of subscripts = 1
Sum of subscripts = 2

## Slide 32: Multiplying polynomials is equivalent to convolving coefficients!
If:
F(z) = z-transform of G(z) = z-transform of then: F(z)G(z) = z-transform of

## Slide 33: Convolution in time domain = multiplication in z-domain
f0, f1, f2, …
g0, g1, g2, …
f g
Convolve
Z-transform
F(z)
G(z)
F(z)G(z)
Multiply
Z-transform
Time domain
“z” domain
Notes: Convolving in TIME domain is equivalent to multiplying in Z domain.
You can take two time series, f and g, and convolve them to get a third time series.
Or you can take the z-transforms of f and g, multiply them, and you’ll get something that is the z-transform of the convolved time series.

## Slide 34: What is this z-transform?

## Slide 35: z can be any number. What if z = 1?
F(z) = f0 + f1z + f2z2 + f3z3 + …
F(1) is sum of coefficients:

## Slide 36: What if: ?
Remember:
Notes: Everywhere we see a “z”, we plug in exp(-2pi*i/N).
Raising an exponential to a second exponential just causes the exponents to multiply.

## Slide 37: Euler’s identity:
Notes: I set N = 100 arbitrarily here. Obviously, it can be anything.

## Slide 38: A familiar dot product

## Slide 39: A familiar dot product

## Slide 40: Keep going …
Where k = 0, 1, … N-1
Etc…
zkn are k-cycle sinusoids.
z0n
z1n
z2n
z3n
z4n
z5n
z6n
z7n
z8n
z9n
n = 0 to N-1

## Slide 41: Put all these z tranforms together = Fourier!
Plug in:
Notes: Actually, the F(z) formulation is slightly more flexible, in that we can evaluate it for values of k that are not integers 0 … N-1.

## Slide 42: Time and “z” domains
f[t] = f0, f1, f2, …
g[t] =g0, g1, g2, …
f[t] g[t]
Convolve
Z-transform
F(z)
G(z)
F(z)*G(z)
Multiply
Z-transform
Time domain
Z domain
Notes: If you want to convolve A with the sum of B and C, you can break it into two easier tasks. First convolve A with B, then A with C, then add the two results.
All linear functions are handy this way, they can always be broken down into parts, solved independently, then added back together.

## Slide 43: But the Fourier transform is a special case of the z transform
f[t] = f0, f1, f2, …
g[t]=g0, g1, g2, …
f[t] g[t]
Convolve
Z-transform
Fourier transform
FFT(f)
FFT(g)
FFT(f)*FFT(g)
Multiply
Z-transform
Fourier transform
Time domain
Z Frequency domain
Notes: If you want to convolve A with the sum of B and C, you can break it into two easier tasks. First convolve A with B, then A with C, then add the two results.
All linear functions are handy this way, they can always be broken down into parts, solved independently, then added back together.

## Slide 44
Convolve
FFT
FFT(f)FFT(g)
Multiply
FFT
Time domain
Frequency domain
FFT
Notes: Not optimal

## Slide 45: Application: “deconvolve” by dividing:
Calcium signals reflect spike trains (not directly observable) convolved with exponential decay. Need deconvolution to recover spike train.
(this can’t be observed directly)
(this is what you measure)
Notes: Not optimal

## Slide 46: Application: “deconvolve” by dividing:
Calcium signals reflect spike trains (not directly observable) convolved with exponential decay. Need deconvolution to recover spike train.
(this can’t be observed directly)
(this is what you measure)
Notes: Not optimal

## Slide 47
Calcium signal
Deconvolve
(hard)
Divide
(easy)
Time domain
Frequency domain
Spike train (not observable directly)
FFT
FFT_calcium
FFT
FFT
FFT_decay
Notes: Not optimal

## Slide 48: A problem …
Divide
Frequency domain
FFT_calcium
Might end up dividing by 0, or nearly 0
Notes: Not optimal

## Slide 49: Weiner deconvolution
Notes: Not optimal

## Slide 50: Another application
In previous example, we used Matlab to design impulse response based on desired frequency response.
What if we have the opposite – we know the impulse response, but want to figure out the frequency reponse?

## Slide 51: Example: a very common filter, 7-day moving average
Notes: Not optimal

## Slide 52: Moving average is convolution with “boxcar” function
Impulse response
Each value is 1/7 = 0.142857…
Notes: Not optimal

## Slide 53: Take FFT of “boxcar”…
Mostly low-pass.
“Ripples” at higher frequencies
Periodic “nulls” at frequencies 1/7, 2/7, 3/7, etc.
Frequency
Impulse response
Frequency response
= FFT of above pattern
Notes: Not optimal

## Slide 54: Moving average:
“f” = input waveform
“w” = Impulse function
f[t] w[t]
Convolve
FFT
Multiply
FFT
Time domain
Frequency domain
FFT
Notes: Not optimal

## Slide 55: Alternatives to boxcar.
Hamming window:
Passband is about 2x wider than boxcar. But once the response comes down, it stays down.
Wider passband.
Smaller sidelobes

## Slide 56: Can reverse where we do multiplication/convolution
f[t] = f0, f1, f2, …
g[t]=g0, g1, g2, …
f[t] g[t]
Multiply
FFT
FFT(f)
FFT(g)
FFT(f) FFT(g)
Convolve
FFT
Time domain
Frequency domain
Notes: If you want to convolve A with the sum of B and C, you can break it into two easier tasks. First convolve A with B, then A with C, then add the two results.
All linear functions are handy this way, they can always be broken down into parts, solved independently, then added back together.

## Slide 57: Sampling a continuous waveform = multiplication in time domain
Time domain
Frequency domain
Multiply
Convolve
Impulse interval = 1/F
Impulse interval = F
F/2
-F/2

## Slide 58: Homework, due in two weeks (Dec 7, 2020)
Download the following two files to your MATLAB folder.
File #1 is a waveform plus “noise” around 2kHz.
https://www.dropbox.com/s/nvdwd3oeeifcqdb/Homework2.mat?dl=0
https://www.dropbox.com/s/ptwymcr8ynp5hir/Homework2.m?dl=0
File #2 is MATLAB code that loads file #1 and plays audio via speaker.
Task 1: write MATLAB code to remove the noise and identify the underlying musical piece. There should be at least two entirely different ways of removing the noise: one works in time domain, other in frequency domain
Task 2: Plot Fourier transforms of wave before and after filtering.

## Slide 59: Good overview of filtering:
https://www.sciencedirect.com/science/article/pii/S0896627319301746