## Slide 1: Lecture 2: Filters
Tom Jhou

## Slide 2: First: a note about Python function arguments:

## Slide 3: Filters are everywhere. Job is to improve signal detection:
Electronic amplifiers, recording devices
Data analysis software
Biological systems (visual and auditory cortex)

## Slide 4: Example: neural spike detection:
Notes: This works like a charm. Before filtering, the background noise ranges over several millivolts, while spikes are only about 300 microvolts.
After filtering, background noise is about 100 microvolts, while spikes are still about 300 microvolts.
We removed a lot of stuff, and drastically reduced the background noise while spikes are almost the same height as before.

## Slide 5: Imaging examples:
“Edge detection” filter
Notes: This works like a charm. Before filtering, the background noise ranges over several millivolts, while spikes are only about 300 microvolts.
After filtering, background noise is about 100 microvolts, while spikes are still about 300 microvolts.
We removed a lot of stuff, and drastically reduced the background noise while spikes are almost the same height as before.

## Slide 6: How do you define “signal” vs “noise”?
Depends on your goal.
“Noise” in one experiment may be “signal” in another.

## Slide 7: Example: find action potentials in brain recording
Notes: There are fast wiggles and slow wiggles. The background noise tends to have lots of slow wiggles, the spikes tend to have lots of fast wiggles. We can use this to our advantage.
There are 20,000 points shown. The sampling rate is 31.25kHz, so this is about 2/3 of a second in the top part, and 1/8 second in the bottom part.

## Slide 8: Perform “spectral analysis” of spikes vs noise
Spikes
Background “noise”
Notes: “Noise” is in quotation marks because it actually is a brain signal. It comes from neurons that are too far away from recording wire to be resolved independently.

## Slide 9: Noise is predominantly low-frequency. If we remove it, spikes will “stick out” more.
Spikes
Background “noise”
Notes: “Noise” is in quotation marks because it actually is a brain signal. It comes from neurons that are too far away from recording wire to be resolved independently.

## Slide 10: How did we do this frequency analysis? FFT = “Fast Fourier Transform”
import numpy as np
y = np.fft.fft(waveform);
waveform = list of voltages at regular time intervals
y = list of amplitudes at regular frequency intervals
Notes: The function is easy to call, but you have to pay careful attention to the details of the frequencies that come out.

## Slide 11: FFT of sine wave …
Input is a 1-second segment of a
5 Hz sine wave, sampled at 100Hz
FFT has peaks at 5 Hz and 95 Hz
5Hz makes sense. Ignore the 95Hz peak for now. Will explain in a few minutes.
waveform
FFT
Notes: The function is easy to call, but you have to pay careful attention to the details of the frequencies that come out.

## Slide 12: FFT of square wave:
Input is 5 Hz square wave, sampled at 100Hz
FFT has peaks at odd multiples of 5Hz: 5, 15, 25, et … Hz
Note symmetry at 50Hz
waveform
FFT
Notes: The function is easy to call, but you have to pay careful attention to the details of the frequencies that come out.

## Slide 13: Square wave can be viewed as an infinite sum of sinusoids
Amplitude
Notes: Note that the sine wave amplitudes are exactly inversely proportional to the frequency, i.e. they get smaller as frequency goes up. The “discrepancy” between sinusoidal sum and “true” square wave gets smaller and smaller as well.

## Slide 14: By altering phase, amplitude, we can get triangle, sawtooth waves
Square wave: odd harmonics, nth harmonic has amplitude 1/n.
Triangle wave: odd harmonics, amplitude 1/n2
Sawtooth: sines instead of cosines, odds + evens
Notes: Note that the sine wave amplitudes are exactly inversely proportional to the frequency, i.e. they get smaller as frequency goes up. The “discrepancy” between sinusoidal sum and “true” square wave gets smaller and smaller as well.

## Slide 15: By modifying phase and amplitude, can build any waveform
https://www.youtube.com/watch?v=ds0cmAV-Yek
Notes: Destin doesn’t explain one very critical item, which is that the rotational speeds of the various circles are all FIXED INTEGER MULTIPLES of each other. The first circle rotates at some constant speed. The second circle rotates at twice that speed, the third circle rotates at 3 times the speed, and so on. The shape is entirely defined by the diameters (amplitudes) of the circles.

## Slide 16: FFT of neural recording
Spikes
EEG
Notes: There are fast wiggles and slow wiggles. The background noise tends to have lots of slow wiggles, the spikes tend to have lots of fast wiggles. We can use this to our advantage.
There are 20,000 points shown. The sampling rate is 31.25kHz, so this is about 2/3 of a second in the top part, and 1/8 second in the bottom part.

## Slide 17: Log vs Linear axes:
Spikes
EEG
Log axes – can see small numbers well
Spikes
EEG
Linear axes
(small numbers all smushed together)
Notes: “Noise” is in quotation marks because it actually is a brain signal. It comes from neurons that are too far away from recording wire to be resolved independently.

## Slide 18: Linear axes show absolute distance, Log axes show relative change
10-fold
range
10-fold
range
10-fold
range
400Hz
range
400Hz
range
400Hz
range
400Hz
range
Notes: “Noise” is in quotation marks because it actually is a brain signal. It comes from neurons that are too far away from recording wire to be resolved independently.

## Slide 19: Noise has a lot of low frequencies (slow wiggles). Can remove them with “high-pass” filter.
Spikes
Background
Removing low frequencies will get rid of a LOT of background, but much less signal

## Slide 20: Filters are never perfect. There is “transition” from “pass” to “stop” bands
Output in the stop band is lower, but not zero.

## Slide 21: Note the “decibel” notation:
dB = 20 * log_10.
Why 20, and not 10?
Because power = amplitude2, so 10x amplitude increase gives 100x power increase.

## Slide 22: 3dB is the “half power” point:
This is where amplitude is 70.7% of max.
20 * log(0.707) = -3.01
Power = amplitude2, and (0.707)2 = 0.5

## Slide 23: Other standard filter types
Any shape is possible, e.g. multiple pass bands, or arbitrary shapes.
“Roll-off” rate varies with filter type - can be shallow or steep.

## Slide 24: Before vs after:
w = fir1(n, cutoff_frequency*2/sampleRate, ‘high’)
output = conv(input_signal, w);
Notes: This works like a charm. Before filtering, the background noise ranges over several millivolts, while spikes are only about 300 microvolts.
After filtering, background noise is about 100 microvolts, while spikes are still about 300 microvolts.
We removed a lot of stuff, and drastically reduced the background noise while spikes are almost the same height as before.

## Slide 25: Voltage histograms
Spike peaks
Background
Background
Spikes
Voltage (mV)
Voltage (mV)
Before filtering
After filtering
False positives
True positives
False negatives
True negatives
Detection threshold
Notes: These are histograms of the voltage ranges. Before filtering, background and spikes range over several millivolts, and overlap.
After filtering, spike peaks are separable from background voltages. We can draw a somewhat arbitrary vertical threshold (blue dotted line) that “detects” most of the spikes while “rejecting” most of the background.

## Slide 26: Log vs linear plots. >99.99% separation
Spike peaks
Background
Voltage (mV)
False positives
True positives
Detection threshold
More selective
More permissive
Detection threshold
~99.99% separation
Background
Spike peaks
Log probability density
Probability (linear)
False negatives
True negatives
Notes: These are histograms of the voltage ranges. Before filtering, background and spikes range over several millivolts, and overlap.
After filtering, spike peaks are separable from background voltages. We can draw a somewhat arbitrary vertical threshold (blue dotted line) that “detects” most of the spikes while “rejecting” most of the background.

## Slide 27: 99.99% separation is awesome. Let’s look at a noisier example:
Spikes
Background
Voltage (mV)
Detection threshold
More selective
(Fewer false positives,
but also more false negatives)
More permissive
Fewer false negatives,
but also more false pos.)
False negatives
True negatives
Notes: These are histograms of the voltage ranges. Before filtering, background and spikes range over several millivolts, and overlap.
After filtering, spike peaks are separable from background voltages. We can draw a somewhat arbitrary vertical threshold (blue dotted line) that “detects” most of the spikes while “rejecting” most of the background.

## Slide 28: “Receiver operator characteristic” (ROC) expresses tradeoff
Background
Voltage (mV)
Detection threshold
More selective
(Fewer false positives,
but also more false negatives)
More permissive
Fewer false negatives,
but also more false pos.)
More selective
More permissive
False positives
True positives
Spikes
Notes: These are histograms of the voltage ranges. Before filtering, background and spikes range over several millivolts, and overlap.
After filtering, spike peaks are separable from background voltages. We can draw a somewhat arbitrary vertical threshold (blue dotted line) that “detects” most of the spikes while “rejecting” most of the background.

## Slide 29: “Receiver operator characteristic” (ROC) expresses tradeoff
Spikes
Voltage (mV)
True positives
Detection threshold
More selective
(Fewer false positives,
but also more false negatives)
More permissive
Fewer false negatives,
but also more false pos.)
More selective
More permissive
False positives
Background
Notes: These are histograms of the voltage ranges. Before filtering, background and spikes range over several millivolts, and overlap.
After filtering, spike peaks are separable from background voltages. We can draw a somewhat arbitrary vertical threshold (blue dotted line) that “detects” most of the spikes while “rejecting” most of the background.

## Slide 30: Filtering greatly improved detection, but still far short of perfection
More selective
More permissive
y=x, random classification
Detecting ~25% of spikes, and ~5% of noise.
Highest signal/noise ratio (5:1).
Perfect classification:
Detect 100% of signal, 0% of background.
Can’t get here with this dataset.
p = 0.05 (publication standard)
Before filtering
After filtering
Notes: These are histograms of the voltage ranges. Before filtering, background and spikes range over several millivolts, and overlap.
After filtering, spike peaks are separable from background voltages. We can draw a somewhat arbitrary vertical threshold (blue dotted line) that “detects” most of the spikes while “rejecting” most of the background.

## Slide 31: Filtering is big help, but to go further you usually need a better experiment (e.g. better technology, or move probe closer to neurons)

## Slide 32: Area under curve (AUC) is proportional to Mann-Whitney “U”
Notes: These are histograms of the voltage ranges. Before filtering, background and spikes range over several millivolts, and overlap.
After filtering, spike peaks are separable from background voltages. We can draw a somewhat arbitrary vertical threshold (blue dotted line) that “detects” most of the spikes while “rejecting” most of the background.

## Slide 33: Python code:
w = scipy.signal.firwin(n, cutoff_frequency*2/sampleRate, pass_zero = True)
output = np.conv(input_signal, w);

## Slide 34: “firwin” arguments:
w = scipy.signal.firwin(n, cutoff_frequency*2/sampleRate, pass_zero=True)
n is filter “order”
cutoff_frequency is half-power frequency (transition from pass to stop bands)

## Slide 35: “firwin” arguments:
w = scipy.signal.firwin(n, cutoff_frequency*2/sampleRate, pass_zero=True)
pass_zero = True for a low-pass filter, False for high-pass
True
False

## Slide 36: “conv” function arguments:
w = fir1(n, cutoff_frequency*2/sampleRate, pass_zero=True)
output = np.convolve(input_signal, w);
“w” is the “impulse function”
“convolve” takes two inputs, and produces a filtered output.

## Slide 37: Higher filter order n gives sharper transition
N=5
N=100
N=20
N=2
N=10

## Slide 38: Low-pass filter
N=5
N=100
N=2

## Slide 39: But: high order filters produce delays and other distortions
Before
filter
After
filter
Output is time-delayed (easy to compensate).
Biphasic waveform might become triphasic (NOT easy to correct)
High-order filters distort more than low order
High-pass filters distort more than low-pass.
Notes: The original spike (brown) is shifted in time and is now triphasic instead of biphasic. Actually, it is almost quadruphasic, as there is a slight backlash to the initial AHP.
The time shift is easy to fix – just subtract. The distortion is much harder to fix. Theoretically you can run it back through a lowpass filter, but that brings back some of the noise you got rid of.
Distortion may or may not be a problem. This depends on the question you are asking. If you just want to know firing rate and spike latency, you don’t have to worry.

## Slide 40: Another distortion:
Real-world signals (from the brain) are continuous, but computers process signals that are “sampled” at a finite rate
time
time

## Slide 41: “Aliasing” occurs if sample rate is too low
Sine wave = 10kHz.
Sample rate = 40kHz (4x)
GOOD!
Sine wave = 30kHz.
Sample rate = 40kHz (1.33x)
BAD!
Notes: Note that the 30kHz wave looks exactly like the 10kHz wave when sampled at 40kHz. This is the “aliasing”, where one wave looks like another.

## Slide 42: Aliasing
At 40kHz sample rate,
10kHz, 30kHz look same
5kHz, 35kHz look same
1Hz, 33,999Hz look same
x and 40kHz – x
Max detectable frequency is 20 kHz: “Nyquist” frequency

## Slide 43: Typically need analog filter before digital sampling
https://community.sw.siemens.com/s/article/data-acquisition-anti-aliasing-filters
Low-pass ANALOG filter

## Slide 44: If frequencies < Nyquist, original wave can be interpolated perfectly from samples (via sinc function)
https://demonstrations.wolfram.com/SincInterpolationForSignalReconstruction/
Blue = original signal. Red dots = sampled.
Magenta = interpolated from samples using sinc function.

## Slide 45: Homework, due in 1 week
Update the github repository. You should see a folder called Class2, and a Python file called Homework2.py
Task 1: write code to remove the noise and identify the underlying musical piece.
Task 2: Plot Fourier transforms of wave before and after filtering.

## Slide 46: The end. Ignore any slides after this one.

## Slide 47: The code:
% Generate/plot 5 Hz square wave
t = np.arange(100)/100
y = scipy.signal.square(t*5*2*pi);
np.step(t, y)
% Calculate/plot FFT
f = np.fft.fft(y);
np.plot(abs(f))
waveform
FFT
Notes: The function is easy to call, but you have to pay careful attention to the details of the frequencies that come out.

## Slide 48: Convolution, FFT, are all “linear” functions

## Slide 49: Much of nature is non-linear
But non-linear math is freakishly complex, so we try to make linear approximations wherever possible.
Many things are linear, up to a point.

## Slide 50: Algebraic definition of linearity:
  All terms square and higher are zero:

## Slide 51: Most general definition of linearity
A function f is linear if and only if:
  f(x + y) = f(x) + f(y) f (of sums) = sum (of f’s)
  af(x) = f(ax) Scalability
Notes: If you want to convolve A with the sum of B and C, you can break it into two easier tasks. First convolve A with B, then A with C, then add the two results.
All linear functions are handy this way, they can always be broken down into parts, solved independently, then added back together.

## Slide 52: Good overview of filtering:
https://www.sciencedirect.com/science/article/pii/S0896627319301746

## Slide 53: Why “abs”?
% Calculate/plot FFT
f = fft(y);
plot(abs(f))
FFT
Notes: The function is easy to call, but you have to pay careful attention to the details of the frequencies that come out.