## Slide 1: Lecture 3: Convolution
Tom Jhou
2021

## Slide 2: Recall these two magic functions:
kernel = scipy.signal.firwin(n, cutoff_frequency*2/sampleRate, pass_zero=False)
output = np.convolve(input_signal, kernel);
Notes: This works like a charm. Before filtering, the background noise ranges over several millivolts, while spikes are only about 300 microvolts.
After filtering, background noise is about 100 microvolts, while spikes are still about 300 microvolts.
We removed a lot of stuff, and drastically reduced the background noise while spikes are almost the same height as before.

## Slide 3: np.convolve()takes two input vectors and produces a third
kernel = scipy.signal.firwin(n, cutoff_frequency*2/sampleRate, pass_zero=False)
output = np.convolve(input_signal, kernel)
Output vector.
Input vector
Kernel … another vector independent of in/out
In a sense, the kernel “defines” the filter. If you change the filter type (e.g. highpass vs lowpass, filter order, cutoff frequency) you will get a different kernel, and vice versa.
Notes: Back to our regularly scheduled programming …

## Slide 4: The magic kernel is just a vector, i.e. list of numbers. Can plot it like any other vector, but it won’t give you any insight.
High-pass
Low-pass
Band-stop
Notes: High-order filters often have very “ringy” impulse responses. This will cause waveform distortion. If that is a problem, then it’s best to redesign the experiment to use lower order filters.

## Slide 5: But wait … the length equals the filter order. Interesting …
Order = 501
Notes: High-order filters often have very “ringy” impulse responses. This will cause waveform distortion. If that is a problem, then it’s best to redesign the experiment to use lower order filters.

## Slide 6: We will use this weird symbol to denote convolution:
Output =
Most texts use asterisk * . ⨂ is less common, but avoids confusion with multiplication
Notes: To understand what a mathematical operation is doing, always, always, always, go to the formula. Even the best verbalized descriptions of math are merely approximations, that will likely miss key aspects of what is being done.

## Slide 7: Remember that waves in a computer are samples at regular time intervals:
x[t]
t
Notes: To understand what a mathematical operation is doing, always start with the formula, then go to geometry.
Verbalized descriptions are almost never adequate, will not be precise enough.
Incidentally, in texts that use asterisk for convolution, then multiplication needs to use a dot, or nothing at all, to avoid confusion.

## Slide 8: So waveforms are also “functions”, of sample number t:
x[t]
t
Notes: To understand what a mathematical operation is doing, always start with the formula, then go to geometry.
Verbalized descriptions are almost never adequate, will not be precise enough.
Incidentally, in texts that use asterisk for convolution, then multiplication needs to use a dot, or nothing at all, to avoid confusion.

## Slide 9: Functions in math, Python, MATLAB, etc are basically this:
Notes: To understand what a mathematical operation is doing, always start with the formula, then go to geometry.
Verbalized descriptions are almost never adequate, will not be precise enough.
Incidentally, in texts that use asterisk for convolution, then multiplication needs to use a dot, or nothing at all, to avoid confusion.

## Slide 10: Here is a simpler example:
Notes: To understand what a mathematical operation is doing, always start with the formula, then go to geometry.
Verbalized descriptions are almost never adequate, will not be precise enough.
Incidentally, in texts that use asterisk for convolution, then multiplication needs to use a dot, or nothing at all, to avoid confusion.

## Slide 11: So …
Rule:
if input = 0, then output = 1
if input = 1, then output = 1
If input = 2, then output = 2
If input = 3, then output = 2
If input = 4, then output = 1
If input = 5, then output = 0
x values
y values
Notes: To understand what a mathematical operation is doing, always start with the formula, then go to geometry.
Verbalized descriptions are almost never adequate, will not be precise enough.
Incidentally, in texts that use asterisk for convolution, then multiplication needs to use a dot, or nothing at all, to avoid confusion.

## Slide 12: Of course, we can also represent this “rule” as a vector:
In Python:
x = np.array([1, 1, 2, 2, 1, 0])
Notes: To understand what a mathematical operation is doing, always start with the formula, then go to geometry.
Verbalized descriptions are almost never adequate, will not be precise enough.
Incidentally, in texts that use asterisk for convolution, then multiplication needs to use a dot, or nothing at all, to avoid confusion.

## Slide 13: Let’s use “[t]” to turn waveforms into functions:
where t = 0, 1, 2, …
Notes: To understand what a mathematical operation is doing, always start with the formula, then go to geometry.
Verbalized descriptions are almost never adequate, will not be precise enough.
Incidentally, in texts that use asterisk for convolution, then multiplication needs to use a dot, or nothing at all, to avoid confusion.

## Slide 14: Let’s abbreviate, or else the screen will soon fill up with long words …
Notes: To understand what a mathematical operation is doing, always start with the formula, then go to geometry.
Verbalized descriptions are almost never adequate, will not be precise enough.
Incidentally, in texts that use asterisk for convolution, then multiplication needs to use a dot, or nothing at all, to avoid confusion.

## Slide 15: Mathematical definition of f g:
This is just plain old multiplication.
Notes: To understand what a mathematical operation is doing, always start with the formula, then go to geometry.
Verbalized descriptions are almost never adequate, will not be precise enough.
Incidentally, in texts that use asterisk for convolution, then multiplication needs to use a dot, or nothing at all, to avoid confusion.

## Slide 16: Summation notation:
= 12 + 22 + 32 + 42 + 52
= 1 + 4 + 9 + 16 + 25
= 55
Notes: To understand what a mathematical operation is doing, always start with the formula, then go to geometry.
Verbalized descriptions are almost never adequate, will not be precise enough.
Incidentally, in texts that use asterisk for convolution, then multiplication needs to use a dot, or nothing at all, to avoid confusion.

## Slide 17: Let’s assume f(t) applies to positive time only:
f(t) = 0 for t < 0, i.e. we have input at positive time only

## Slide 18: Let’s assume kernel also applies to positive time only:
g(t) = 0 for t < 0, i.e. kernel has positive time only

## Slide 19: Now summation limits are much easier …
Notes: To understand what a mathematical operation is doing, always, always, always, go to the formula. Even the best verbalized descriptions of math are merely approximations, that will likely miss key aspects of what is being done.

## Slide 20: Let’s evaluate output at t = 0:

## Slide 21: Let’s evaluate output at t = 1:

## Slide 22: Let’s evaluate output at t = 2:
Every index
pair sums to 2

## Slide 23: Let’s evaluate output at t = 5:
Every index
pair sums to 2

## Slide 24: Subscripts at right always sum to t:
Subscripts sum to t
k + (t – k) = t
Notes: To understand what a mathematical operation is doing, always, always, always, go to the formula. Even the best verbalized descriptions of math are merely approximations, that will likely miss key aspects of what is being done.

## Slide 25: t = 6

## Slide 26: How to visualize this?
Draw pairwise products on a grid …
 | g[0] | g[1] | g[2] | g[3]
f[0] | f[0]*g[0] | f[0]*g[1] | f[0]*g[2] | f[0]*g[3]
f[1] | f[1]*g[0] | f[1]*g[1] | f[1]*g[2] | f[1]*g[3]
f[2] | f[2]*g[0] | f[2]*g[1] | f[2]*g[2] | f[2]*g[3]
f[3] | f[3]*g[0] | f[3]*g[1] | f[3]*g[2] | f[3]*g[3]
t = 0
t = 1
t = 2
t = 3

## Slide 27: Convolution is commutative.
Switching f, g flips grid diagonally = same answer
 | g[0] | g[1] | g[2] | g[3]
f[0] | f[0]*g[0] | f[0]*g[1] | f[0]*g[2] | f[0]*g[3]
f[1] | f[1]*g[0] | f[1]*g[1] | f[1]*g[2] | f[1]*g[3]
f[2] | f[2]*g[0] | f[2]*g[1] | f[2]*g[2] | f[2]*g[3]
f[3] | f[3]*g[0] | f[3]*g[1] | f[3]*g[2] | f[3]*g[3]
Sum of subscripts = 0
Sum of subscripts = 1
Sum of subscripts = 2
Notes: Will leave this as an exercise for the reader to prove …

## Slide 28: Visualization #2: Divide and conquer.
Break f into small pieces.
Convolve each piece with g.
Add results back together.

## Slide 29: Break waveform into pieces …
Waveform g[t] =
[g0, g1, g2, g3, g4]
Break into sum of “lollipops”, one for each time value
g0
g1
g2
g3
g4
Notes: Any waveform is just a list of values at consecutive points in time (evenly spaced samples).
So we can break a waveform into a set of waveforms, each of which is non-zero at only a single time point.

## Slide 30: “Lollipop” = delta function
5
when
when
Can shift time/amplitude, e.g.:
5δ[t – 2] = 5 when
5δ[t – 2] = 0 when
Notes: Believe it or not, there is a special name for a function consisting of a single value at a single time point. This sounds like a rather boring function. But it’s a very useful building block

## Slide 31: f = sum of deltas
f0δ[t]
f1δ[t-1]
f2δ[t-2]
f3δ[t-3]
f4δ[t-4]
f0
f1
f2
f3
f4
g[] = ???

## Slide 32: Divide and conquer …
f0δ[t]
f1δ[t-1]
f2δ[t-2]
f3δ[t-3]
f4δ[t-4]
f0
f1
f2
f3
f4
g[] = ???
g[] = ???
g[] = ???
g[] = ???
g[] = ???
g[] = ???

## Slide 33: What is ?
Replace f with δ:
The delta function just disappeared!
Notes: Notice that if f is a delta function, then it effectively disappears from the output.
But is convolution just a black hole, that “eats” functions and makes them disappear?
That would not be useful, would it?

## Slide 34: What if delta is shifted in time?
Let f[k] = δ[k - 2]:
The output is g shifted by 2
@ k = 2, we get:
Notes: Let f be a scaled, shifted, delta function.
When we write out the equations, we see that the scale factor persists. We still throw away the sum at most values of k, but instead of k=0 being the one we throw away, it is k = 987, because that is where the delta function argument becomes zero.
Hence, convolving a scaled, shifted, delta with g transfers the scale and the shift to g. I.e. g becomes time-shifted and scaled by the same amount as the delta function.
Now this is interesting. Convolution produces an output function that exhibits properties (in time and amplitude) of BOTH inputs!

## Slide 35: Example1
Convolve delta with hump,
… get hump
f(t) =
g(t) =
f(t) g(t) =
Notes: Each impulse in the first function gives rise to a scaled, shifted copy of the entire second function, i.e. the “hump”.

## Slide 36: Example2
Convolve shifted delta with hump,
… get shifted hump
f(t) =
g(t) =
f(t) g(t) =
Notes: Each impulse in the first function gives rise to a scaled, shifted copy of the entire second function, i.e. the “hump”.

## Slide 37: Example3
Convolve 2 deltas with hump,
… get two humps, with
f(t) =
g(t) =
f(t) g(t) =
Notes: Each impulse in the first function gives rise to a scaled, shifted copy of the entire second function, i.e. the “hump”.

## Slide 38: Example
Convolve 3 spikes with hump
g(t) =
f(t) =
f(t) g(t) =
Notes: Each impulse in the first function gives rise to a scaled, shifted copy of the entire second function, i.e. the “hump”.

## Slide 39: Overlap …
“Constructive interference”
f(t) =
g(t) =

## Slide 40: Alternation
“Destructive interference”
Slowly changing inputs are augmented.
Fast changing inputs are shrunk
= low-pass filter.
f(t) =
g(t) =

## Slide 41: Example #4
Instead of hump, try this funky shape.
Has positive center spike, and negative “surround”
Notes: Things look reversed now. The low-frequency input produces destructive interference, instead of constructive like before. The high-frequency input produces constructive interference, instead of destructive as we saw before.
This is a simple “high-pass” filter, whereas the previous example was a simple “low-pass” filter.

## Slide 42: Example #4
Slowly changing inputs tend to shrink.
Notes: Things look reversed now. The low-frequency input produces destructive interference, instead of constructive like before. The high-frequency input produces constructive interference, instead of destructive as we saw before.
This is a simple “high-pass” filter, whereas the previous example was a simple “low-pass” filter.

## Slide 43: Example #4
Rapidly changing inputs are augmented.
= high-pass filter.
Notes: Things look reversed now. The low-frequency input produces destructive interference, instead of constructive like before. The high-frequency input produces constructive interference, instead of destructive as we saw before.
This is a simple “high-pass” filter, whereas the previous example was a simple “low-pass” filter.

## Slide 44: The humpey and spikey waves are two “kernals”, which define filter properties
Low-pass kernel
High-pass kernel

## Slide 45: Look at this magic “w” again:
kernel = firwin(n, cutoff_frequency * 2/ sampleRate, pass_zero=False)
output = np.convolve(input, kernel)
If “input” is , “output” will be “kernel”.
“kernel” is the filter’s response to a single impulse, hence it is also called the “impulse response”.

## Slide 46: The end (ignore all slides after this)

## Slide 47: 2-D analog: spatial frequencies

## Slide 48: 2-D Fourier Transform

## Slide 49: 2-D Fourier Transform

## Slide 50: 2-D convolution (low pass)

## Slide 51: 2-D convolution (edge detection)

## Slide 52: Finally, some notes about digitization

## Slide 53: Well, this is unexpected …
Notes: So … 1 is not 1, and 1 minus 1 is not zero. Whaaaaat?

## Slide 54: Digital numbers
Notes: Base two works on powers of 2 instead of powers of 10.

## Slide 55: Counting in binary

## Slide 56: What about fractions?
Notes: Instead of positive powers of two, we have negative powers.

## Slide 57: Example: convert 0.1(decimal) to binary
0.1 (decimal) is 0.00011001100110011 … in binary
An infinite repeating pattern.
0.1 is < 1/2 0
0.1 is < 1/4 0
0.1 is < 1/8 0
0.1 is > 1/16, by 0.0375 1
0.0375 > 1/32 by 0.00625 1
0.00625 < 1/64 0
0.00625 < 1/128 0
0.00625 > 1/256 by 0.00234375 1
0.00234375 > 1/512 by 0.000390625 1
0.000390625 < 1/1024 0
0.000390625 < 1/2048 0
0.000390625 > 1/4096 by 0.000146484375 1
0.000146484375 > 1/8192 by 0.0000244140625 1

## Slide 58: Can’t have infinite bits. How many is practical?
MATLAB uses 64 bit arithmetic. 2^64 = 1.8x1019
But universe is analog. Have to convert to digital, and that can get expensive.
10-bit A/D converter
9.6kHz sample rate
$15.82 from Amazon
18-bit A/D converter
625kHz sample rate
$2,128.00 from
National Instruments

## Slide 59: MATLAB (and many similar programs) use “double precision floating point”
Scientific notation in decimal, e.g. 6.02 x1023
Scientific notation in binary, e.g. 1.00110011 x 10101
Mantissa (52 bits), exponent (11 bits), sign (1 bit)
Total = 64 bits.
Older programs use 32-bit “single-precision” floating point. Back when memory was expensive, this was the default. Now obsolete.

## Slide 60: How many bits do we need?
Limiting factor is usually the digitization, when analog signals are first converted to digital.

## Slide 61: Tradeoff between precision and cost
More bits give more precision, also more cost
Brain signals: EEG ~20mV, spikes ~5-200µV, movement artifacts ~500mV
Range is about 2^17. So 18 bits gives you both EEG and spikes. If you just want one or the other, can use fewer bits.
10-bit A/D converter
9.6kHz sample rate
$15.82 from Amazon
18-bit A/D converter
625kHz sample rate
$2,128.00 from
National Instruments
Notes: The limiting factor is not the computation, but the initial digitization

## Slide 62: Brain signals are small. Can scale up to match input range of device.
Arduino maps 0 - 5 volt inputs to binary values 0 – 1023 (= 29 – 1).
Each binary increment = 5/1024 = ~5mV
Brain signals: EEG ~±10mV.
Can amplify 250x (with analog amplifier), giving ±2.5V. Then add 2.5V to give 0-5V range. Now each binary increment = 5/1024/250 = ~20µV.
But spike signals can range ~5-200µV. Not enough “dynamic range”, i.e. range between biggest and smallest resolvable signals.
Notes: The limiting factor is not the computation, but the initial digitization

## Slide 63: Why not just use analog filters? Until 1980s, this was the norm.
Analog filters
Fast (essentially zero delay).
Can be super cheap. An RC lowpass filter cost < $0.01
But: not flexible. Changing parameters requires soldering or switching different components.
Some designs are nearly impossible to implement (e.g. symmetric impulse function)
Digital filters
Need digitizer (expensive)
Need powerful processor to handle arithmetic (expensive)
But: extremely flexible. Change filter by changing program.
Can implement anything that is mathematically conceivable.

## Slide 64: Review of Euler’s formula:
cosine
sine
Multiplying exponentials adds exponents:
Multiplying complex exponentials = rotation
2π
0
π

## Slide 65: Evaluate F(z) for a 100-term input
Define F(z) = f0 + f1z + f2z2 + … f99z99. Evaluate at
where k = 0, 1, … 99
Real part
Imaginary part
F(z) is dot product of fn with a one-cycle sinusoid.
z0
z1
z2
z99
Notes: So, we are going around an (almost) full circle in 100 steps. Sweet.

## Slide 66: fg = gf
Order does not matter in the end

## Slide 67: Diagonal sum of products:
Assume f[t] and g[t] = 0 for t < 0
 | g[0] | g[1] | g[2] | g[3]
f[0] | f[0]*g[0] | f[0]*g[1] | f[0]*g[2] | f[0]*g[3]
f[1] | f[1]*g[0] | f[1]*g[1] | f[1]*g[2] | f[1]*g[3]
f[2] | f[2]*g[0] | f[2]*g[1] | f[2]*g[2] | f[2]*g[3]
f[3] | f[3]*g[0] | f[3]*g[1] | f[3]*g[2] | f[3]*g[3]
Notes: Suppose I make a table with rows and columns, where the rows are labeled with the elements of f, and the columns labeled with the elements of g. Every element of the table is a product of the corresponding row and column labels.
The convolution of f and g is now the some of the products along the diagonals.
This is easy to see from the equation. But it doesn’t give us much insight into what is really going on.

## Slide 68: Multiplying F(z)*G(z) convolves coefficients of F and G!
F(z)G(z) = f0g0 + (f0g1 + f1g0)z + (f0g2 + f1g1 + f2g0)z2 + …
Coefficients of F(z)*G(z) are diagonal sum of products of the coefficients of F, G, i.e. their convolution!
 | g[0] | g[1] | g[2] | g[3]
f[0] | f[0]*g[0] | f[0]*g[1] | f[0]*g[2] | f[0]*g[3]
f[1] | f[1]*g[0] | f[1]*g[1] | f[1]*g[2] | f[1]*g[3]
f[2] | f[2]*g[0] | f[2]*g[1] | f[2]*g[2] | f[2]*g[3]
f[3] | f[3]*g[0] | f[3]*g[1] | f[3]*g[2] | f[3]*g[3]

## Slide 69: We get a matrix …
F(z) = f0 + f1z + f2z2 + f3z3 + …
Notes: Actually, the F(z) formulation is slightly more flexible, in that we can evaluate it for values of k that are not integers 0 … N-1.

## Slide 70: Divide-and-conquer is possible because of linearity …
A
B
A + B
1. Sum first
2. Then convolve with C
1. Convolve with C
A C
B C
A C + B C
=
(A + B) C
2. Then sum
Notes: Linearity looks like the distributive property you learned for ordinary multiplication, which is a special case of linearity.

## Slide 71: Formal definition of linearity
A function f is linear if and only if:
  f(x + y) = f(x) + f(y)
  af(x) = f(ax)
Notes: If you want to convolve A with the sum of B and C, you can break it into two easier tasks. First convolve A with B, then A with C, then add the two results.
All linear functions are handy this way, they can always be broken down into parts, solved independently, then added back together.